## Slide 1
ProteinProcessIO
A GPU-Accelerated Digital Twin for Multi-Stage Dry Air Classification of Plant Proteins
High-Fidelity Multiphysics Simulation | NVIDIA Warp GPU | Interactive Desktop App
From Thermal Pretreatment to Protein Separation — End-to-End Process Design

## Slide 2
Introduction — What is ProteinProcessIO?
Physics-based digital twin for the complete dry fractionation pipeline: RF Thermal Pretreatment, Pin Milling, Air Classification.
Interactive desktop application with real-time 3D visualization.
Enables design, simulate, optimize, and validate industrial classification systems in software before physical prototypes.
Why it matters: Plant-based protein demand is growing; dry fractionation is the most sustainable extraction (no water, no chemicals). ProteinProcessIO replaces expensive trial-and-error with computer-aided engineering.

## Slide 3
The Problem — Challenges in Dry Protein Fractionation
Complex, coupled physics — particle separation depends on aerodynamics, PSD, material properties, and geometry interacting simultaneously.
No integrated simulation tools — engineers rely on spreadsheets, correlations, or single-component CFD that miss cross-stage effects.
Expensive physical prototyping — each pilot trial costs thousands; iterating is slow.
Multi-stage coupling — pretreatment affects milling, which affects PSD, which determines classification. Optimizing one stage in isolation is suboptimal.
Competing objectives — protein purity vs. yield; thermal treatment for flavor vs. protein denaturation risk.
The gap: No software combines parametric geometry + multiphysics + GPU + multi-objective optimization for food powder classification.

## Slide 4
Objective, Research Questions & Hypothesis
Objective: Develop a GPU-accelerated, physics-based digital twin for computer-aided design and optimization of multi-stage dry air classification — from thermal pretreatment through milling to protein–starch separation.
Research questions: (1) Can coupled multiphysics (RF + particle dynamics + fluid) predict real equipment when calibrated with sensor data? (2) Can GPU (NVIDIA Warp) make 3D simulation fast enough for interactive exploration? (3) Can multi-objective optimization (Derringer–Suich) identify optimal conditions for yield, purity, energy, and quality?
Hypothesis: A physics-based digital twin calibrated against PLC sensor data will predict classification performance within engineering accuracy (<15% error), with GPU enabling interactive runs (<5 min per full simulation).

## Slide 5
Methods Overview — Digital Twin Methodology
Parametric 3D geometry (40+ parts) → Multiphysics simulation (GPU-accelerated) → Calibration with PLC sensor data.
Outputs feed: Interactive desktop GUI ← Multi-objective optimization ← Validated digital twin.
Why physics-based over ML: Lower data requirement; reliable extrapolation; interpretable; supports new materials and scale-up; design exploration; regulatory trust.

## Slide 6
Methods — Three-Stage Coupled Pipeline
Stage 1 — RF Pretreatment (GP-15): Laplace (E-field), heat equation (T), diffusion (M), dielectric properties, PLC logic, belt advection. 9-step coupling per timestep.
Stage 2 — Pin Milling: Impact detection, breakage model (selection + breakage function), screen passage, population balance.
Stage 3 — Air Classification: Zone-based Lagrangian tracking — Venturi eductor, zigzag classifier, wheel classifier (300–5000 g), 3-stage cyclones, bag filter. Drag: Stokes, Schiller–Naumann, Haider–Levenspiel.

## Slide 7
Methods — Calibration with Real Hardware (GP-15)
Strategy: Match PLC sensors (temperature, RF current, belt speed, moisture) and temp strips to simulation under same operating conditions; tune oscillator efficiency, contact resistance, convection.
GP-15 Run#2 validation: 90 kg yellow pea, 35 mm bed, 0.2 m/min, electrode gap 75→94 mm. Outfeed 68–82°C, moisture loss 1.3 pp, LOX inactivation 24.2 min above 65°C, specific energy 0.042 kWh/kg.
Calibration store: Empirical curves and tuned parameters saved for reuse across operating conditions.

## Slide 8
Calibration Innovations — GP-15 Digital Twin (Technical Note)
Result | Detail
Four-parameter calibration | k_c, k_evap, r_gap, k_disp via differential evolution + L-BFGS-B on full PLC tim
Electrode gap prediction | Run#2 blind: 93.0 mm sim vs 94.1 mm PLC — 1.2% error; validates EM + control cha
Energy partition | 99.2% sensible heating, ~0.8% latent; seed coat suppresses evaporation at sub-10
MRH edge regime | Anode current ~1.70 A near threshold; proportional gap drift correctly predicted
Sensor-comparable metric | 75th percentile outfeed T for PLC/strip comparison; P75 vs mean vs max
GPU performance | 57,600 cells; ~3 s/eval; calibration 926 evals in ~46 min; 60× speedup with arra

## Slide 9
Methods — Python Technology Stack
GUI: PySide6 (Qt6) + PyVistaQt — 3D viewport, mode switching (Classification / Pretreatment / Milling), cinematic camera, live KPI dashboards.
Visualization: PyVista (VTK) — 40+ parametric meshes, real-time particles, physics-driven animations.
Simulation: NumPy, SciPy, NVIDIA Warp — coupled solvers, Lagrangian tracking, zone-based classification, SPH air flow.
GPU: NVIDIA Warp (JIT CUDA) — 10+ kernels, persistent GPU memory, batched launch, single sync.
Data: Pandas, Matplotlib, PyYAML — CSV/JSON/VTK export, publication plots. Packaging: PyInstaller for standalone executable.

## Slide 10
Methods — NVIDIA Warp GPU Acceleration
Warp: Python framework; @wp.kernel functions JIT-compiled to CUDA; vec3, mat33, Mesh, HashGrid; automatic CPU/CUDA fallback.
Kernels per timestep (batched, single sync): RF field, thermal, moisture, dielectric, transport, particle (drag, collisions, zone tracking).
Strategy: Persistent GPU arrays, batched launch, one wp.synchronize() per step, kernel cache. Advantage vs raw CUDA: pure Python syntax, fast iteration, NumPy/SciPy interop, maintainable by non-GPU specialists.

## Slide 11
Methods — Multi-Objective Optimization (Derringer–Suich)
Pretreatment: 5 objectives — thermal treatment (65–82°C), LOX kill (≥4 min above 65°C), protein preservation (peak <71°C vicilin), moisture retention (<2 pp loss), energy (<0.15 kWh/kg). Overall desirability = geometric mean; scaled 0–10.
Material-specific profiles: Yellow pea (7S <71°C), faba bean (11S <90°C), red lentil (<75°C).
Classification: Design variables — wheel RPM, cyclone diameters, air flow. Objectives — maximize yield and purity, minimize energy; constraints on efficiency and starch purity.

## Slide 12
Methods — Integrated Environmental & Economics
End-to-end: Raw seeds → RF Pretreatment → Pin Milling → Air Classification. Energy per stage tracked; zero water, zero chemical waste.
Environmental: Energy per kg, carbon from energy source; economic: capex from parametric geometry, energy cost per kg, yield (protein vs starch), throughput for capacity planning.
Dry vs wet: Dry ~0.05–0.10 kWh/kg, 0 L water/kg, 50–65% purity; wet ~0.3–0.5 kWh/kg, 5–10 L water/kg, 80–90% purity. Digital twin enables per-stage accounting and Pareto yield–purity curves.

## Slide 13
Methods — Desktop Application (PyInstaller)
Standalone executable; three-mode interface (Classification, Pretreatment, Milling); real-time 3D viewport (~60 FPS).
Control panel: Material, feed rate, wheel RPM, air flow; live KPIs (efficiency, yield, purity, power); export CSV/VTK.
Physics-driven animations (blower, damper, wheel, belt); cinematic camera (orbit, showcase, flythrough); assembly configurator; live PSD and efficiency curves.

## Slide 14
Results — Pretreatment Validation (GP-15 Run#2)
Metric | Target | Achieved | Status
Outlet temperature | 65–82°C | 68–82°C (PLC + strips) | PASS
LOX inactivation | ≥4 min above 65°C | 24.2 min | PASS
Protein preservation | Max T < 84°C (legumin) | Legumin intact (11S) | PASS
Moisture retention | <2 pp loss | 1.3 pp (11.8%→10.5%) | PASS
Specific energy | <0.15 kWh/kg | 0.042 kWh/kg | PASS

## Slide 15
Results — Classification & Parametric Geometry
Classification (simulated): Cut size ~25 µm @ 3000 rpm; protein yield ~30%, purity ~55%; starch purity ~70%; separation efficiency ~45%.
Parametric geometry: 40+ industrial components, zero hardcoded dimensions; pilot (50 kg/h) to production (2000+ kg/h); dual mesh/SDF for rendering and GPU physics.
GPU: CUDA/CPU auto-detection, persistent memory, batched kernels, <1 ms CPU overhead per step.

## Slide 16
Key Innovations & Breakthroughs
First physics-based digital twin for full dry fractionation (pretreatment + milling + classification) in one coupled simulation.
Whole-seed RF thermal conditioning model: series-capacitor voltage division, Lagrangian tracers; whole seeds show minimal drying (1–2% vs 3–4% for flour).
GPU-accelerated multiphysics in pure Python: 10+ Warp kernels (EM, thermal, moisture, dielectric, particles, advection); near-native CUDA with NumPy/SciPy interop.
Parametric geometry framework: 40+ components from design equations; dual mesh + SDF; automatic scaling.
Multi-objective Desirability (Derringer–Suich); material-specific profiles; interactive desktop with real-time 3D and physics-driven animations.
Calibrated against real GP-15 with PLC data; calibration store for reuse. Comprehensive technical documentation (geometry, multiphysics, Warp, pretreatment guide).

## Slide 17
Summary & Next Steps
Module | Status
RF Pretreatment (GP-15) | Functional — calibrating against Run#2
Hammer Mill (Milling) | In development — geometry and physics in place
Air Classification | Functional — zone-based physics
GUI Application | Functional — 3-mode interface, 3D viewport
Optimization | Framework implemented — expanding to full pipeline

## Slide 18
Next Steps
Complete milling module — breakage mechanics and screen classification.
Full pipeline coupling — end-to-end from seeds to separated protein.
Extended calibration — more experimental runs for validation.
Web documentation portal — installation, user manual, API.
Industrial partner trials — validate at production scale.
Additional materials — oat, chickpea, lentil varieties.

## Slide 19
ProteinProcessIO
Accelerating the future of sustainable plant protein processing through physics-based digital twin technology.
Questions?